## Slide 1
4th year – Electrical Engineering Department
Guillaume VILLEMAUD
Antennas
Basics and Principles of Wireless Communications

## Slide 2
What are we talking about ?
Let’s talk about an antenna (or aerials), an electrical device which converts a guided electric power into free space electromagnetic waves, and vice versa.
There are a multitude of types of antennas, with very various sizes and forms, with more or less complex modes of operation. We will define the features and properties common to these different devices, as well as their areas of application.

## Slide 3
Antennas in everyday life
Analog 800 MHz
DECT ~1900 MHz
Collision avoidance Radar ~80 GHz
Remote Toll ~6 GHz
Lock Remote control 433 MHz
GSM 900 MHz
DCS 1800 MHz
UMTS 2 GHz
LTE 800 MHz, 2.6 GHz
Satellite systems 1 to 45 GHz (Ex : Television 12 GHz, GPS 1.5 GHz)
TV terrestrial 500 MHz
Wifi / Bluetooth / UWB
2.4 à 6 GHz

## Slide 4
Military boat
Wideband antennas for « Electronic war »: listening to foe’s transmissions (radars and comms) for identification and jamming
Communication antennas (HF, VHF, etc.)
Radar antenna for fire control
Radar antennas for missile-launching system
Array antenna for aerial and surface surveillance radar

## Slide 5
Fixed spherical mirror, North-South axis (height of 35 m, length 300 m, surface accuracy 3 mm; radius 560 m)
Plane mobile mirror with an East-West axis(height 40 m ; length 200 m ; surface accuracy 4 mm; weight 700 t)
Antenna focal point, receiving horns and preamplifiers cooled at – 250 °C mobile over an arc of 250 m
Radiotelescope 1 to 3,5 GHz
Nançay Center (Cher, France)

## Slide 6
Main issue: energy
120 dBm
100
80
60
40
20
3 MHz
100m
30 MHz
10m
300 MHz
1m
3 GHz
10 cm
30 GHz
1 cm
300 GHz
1 mm
TV VHF
Amateurs
Amateurs
GSM
TV UHF
Radars (military)
Satellites
Oven
Electronic Toll
DECT
TFTS
0
1W
1mW
1MW
1KW
1GW
Radars (Weather)

## Slide 7
1fW
Isotropic Power
1pW
1µW
1mW
1W
1kW
1MW
1GW
Input Signal
Terrestrial Amplifier
Terrestrial Antenna
Received Signal
AntennaGain
Ampli
Satellite Antenna
Antenna Gain
Low Noise Amplifier
Output Signal
Received Signal on earth
Ex : Earth-Satellite Communication

## Slide 8
Emitter part:
Radio transmission chain
Usefull signal
Mod
Synth.
Cod
antenna
duplexeur
ampli
Circulator
Receiver part:
Usefull signal
Demod
Synth.
Decod
antenna
duplex
ampli
BB
fo
fi
LNA
ampli

## Slide 9
Cellphone example

## Slide 10
Guided Propagation
Guided Propagation
Free space Propagation
Global radio transmission chain:
RF emitter
RF receiver
dig/analog
analog/dig
Radio channel
"Boxes" containing the electronics are connected to the antennas via lines or cables (feeders). From a signal processing perspective, the set of deformations of the wave generated by the wireless + wired transmission form the radio channel.
Concept of Radio channel

## Slide 11
Where do we loose energy?
Impedance mismatch
Impedance mismatch
Propagation environment
Reflections, diffractions, multipaths, obstacles, diffusion, fading, pathloss, weather...
attenuation, dispersion
attenuation, dispersion
Component noises
Component noises
And all these parameters are varying in time, frequency, space and wave polarization…

## Slide 12
Main topics
To properly understand all phenomenon driving antennas behavior, as well as their integration in a complete system, pre-requisites are:
basics of electromagnetism (Maxwell’s equations, EM wave propagation…);
basic knowledge of transmission lines theory and particularly impedance matching principles (progressive or stationary waves..);
take a step back: antennas represent a practical and “visual” application of Maxwell’s theory, building the bridge between purely theoretical equations and real physical phenomenon.